SEPTIC SYSTEM PRIORITY RANKING WORKSHEET

1., 2., 3.     Wastewater discharged through a straight pipe into stream or

man-made means of conveyance (no tank or leach field)	_____

Yes – 500 Points

No – 0 Points

4., 5., 6.     Distance from septic system to a 303(d) listed stream segment or tributary thereof	_____

Less than 100 ft, with >5% slope towards – 400 Points

Between 100 ft and 500 ft, with >5% slope towards – 300 Points

Less than 100 ft, with flat slope – 200 Points

Between 100 ft and 500 ft, with flat slope – 100 Points

More than 500 ft – 0 Points

7.                Soil suitability for absorption (leach) fields (as indicated in NRCS soil survey)	_____

Severe – 200 Points

Moderate – 100 Points

Slight – 0 Points

8.                Distance to any water well	_____

Less than 100 ft.– 200 Points

Between 100 ft. and 500 ft. – 100 Points

More than 500 ft – 0 Points

10.             Impermeable surface such as brick, concrete or asphalt over the leach field – 50 Points	_____

11.             Trees, large shrubs or other plants with extensive root systems

were observed in the vicinity (10 feet) of the leach field – 50 Points	_____

12.             Heavy objects or tracks and impressions directly over the leach field - 50  Points	_____

13.             Signs of System Malfunction

Odors around septic tank or leach field – 50 Points	_____

Ponding or wastewater breakout – 200 Points	_____

Change in color of vegetation in leach field – 50 Points	_____

Pipes exposed at or near ground surface of leach field – 50 Points	_____

Cracks or signs of leakage in risers and lids – 50 Points	_____

14.             Stormwater, sump pumps, foundation drains or roof runoff is

diverted to flow into the septic system – 50 Points	_____

15.             An apparent cave-in or exposed component was identified – 50 Points	_____

18.             Adequacy of septic tank size	_____

| Tank Size | Number of Bedrooms |
| --- | --- |
|  | 1-3 | 4 | 5 |
| <1000 gal | 50 | 100 | 150 |
| 1000 gal | 0 | 50 | 100 |
| 1250 gal | 0 | 0 | 50 |
| 1500 gal | 0 | 0 | 0 |

TOTAL	_____

Comments: